OPTIMA SL6  Operating Instructions

TO SET THE SYSTEM (Turn On) 

The green Day indicator should be showing. Enter your code number. Check that the system is clear (none of the Zone indicators are showing). The sounder will now produce an exit beep tone and you should leave by the approved route. After leaving the protected area it is absolutely essential that you wait until the tone stops, before assuming that the system  has Set. If the system is not clear the sounder will produce a broken beep tone and the fault will be displayed. Either re-enter your code to turn off and investigate or omit the faulty zone (s) from the system. 

TO UNSET THE SYSTEM (Turn Off)

Enter your code. if the system has not been previously activated, the green Day indicator will come on. If the system has been activated, then entering the code will turn the alarm off and the cause of the alarm will be displayed. Press RESET to clear The indication. 

TO OMIT A ZONE

The Day indicator should be showing. Enter your code and the exit tone will start. Press the OMIT button and the exit tone will change to a rapid omit tone. Now enter the zone numbers you wish to omit. For example pressing 2 then 4 will remove zones 2 and 4 from the system. The Zone 2 and Zone 4 indicators will now be showing. If you make a mistake, press 0 to cancel and then enter the correct zone number (s) . When the selection is complete press Set, the exit tone will now continue and you should leave the protected area by the approved route. 
  
CHIME

Chime is a low security monitoring system for use when the system is Unset. When a zone that is set to chime is operated the internal sounder will produce a low volume two stage warning tone and the Zone indicator will show, The indicator may be cancelled by pressing RESET. Chime is particularly useful in a shop to warn of a customers presence or in a house to warn that a door or a particular area you wait until the tone stops. before assuming that the system has been accessed. Any zone may set to be on or off chime by pressing the CHIME key and then keying in the required zone number (s). Key 0 to cancel all zones from chime. After a few seconds the system will automatically return to the Day mode

CODE CHANGE

Press 'Prog', Enter your code, Press '8' Then Enter your new 4-digit code. The new code is now in memory. Press reset to return to day mode.

ALARM MEMORY RECALL

Press Prog and enter your code. Press Chime. The indicator will now scroll to show the last 8 alarm conditions. The sounder will beep as each new condition is shown when complete, press Reset to return to day mode.

NOTE 

A special feature in the SL6, automatically changes the function of zone 2 to become Timed if any zone (s) is omitted when Setting the system.

POWER INDICATOR

The red Power indicator on the control panel should be showing at all times. If the indicator goes off, the mains supply has failed or been disconnected

QUICK SET

During the exit period (after entering your code) the system may be Set quickly by pressing SET. This removes the time period usually allowed for exit and would be used it you are not leaving the premises. If you omit zones and require Quick Set, you will need to press SET twice